## Slide 1: Markov Decision Processes for Hybrid Probabilistic Hierarchical Planning
Presentation by Hatem Htira
Notes: Hello everyone , i m going to speak today about project chimp and how i extended the hybrid planner with spatial solver

## Slide 2: Outline
Background
HTN
CHIMP
Spatial Solver
Solution
The Future Improvement and Conclusion
Operators & Methods
Evaluation
Improving The Spatial Solver Efficiency
Meta-CSP
Limitations
Conversion
Notes: First of all , we hv short overview of the general approach of HTN and meta-CSP
Then i will introduceCHIMP,, and here i will tackle one of limits which the absence of spatial reasoner,
And then other solution to implement spatial solver
And in end we will finish with introducing some possible improvement to CHIMP and introduction

## Slide 3: Hierarchical task network (HTN)
Hierarchical decomposition of plans
Initial plan describes high-level actions
Refine plans using action decompositions
Instead of detecting and cutting unpromising nodes
Process continues until the agent reaches primitive actions
HTN decompose into:
  Compound tasks are tasks that can be decomposed into simpler tasks, implemented using methods
  Primitive tasks are achieved by actions
Notes: Let’s formalize it :
Different level and every high level will be described with sub tasks,

## Slide 4: Decomposition
Compound tasks can be decomposed into simpler tasks
Primitive tasks are achieved by actions
Image 1: HTN decomposition
Notes:   HTN methods are only applierd when the preconditions are satisfied
  Example : go_home  by taxi or by car

## Slide 5: Markov Decision Processes (MDPs)
MDPs are fully observable, probabilistic state models:
Domain is represented as a tuple:
: set of states,
: set of actions.
: reward function
: transition function
discount factor
 Instead of computing a plan, we need a policy.
Notes: Actions cause stochastic transitions. • Actions have costs/rewards.
initial state is known and fully observable ,
and actions are stochastic
describing the reward that the agent receives when it performs action a in state s and ends up in state s

## Slide 6: Example
Notes: 0.8 probability to reach its intended effect
0.2 probability to pick up the wrong object

## Slide 7: Example
Notes: 0.95 probability to reach its intended effect
0.05 probability to move at right angles of the intended direction

## Slide 8: MDPs
Our goal is to find a policy:
Policy is a sequence of applicable actions that maps from initial state s0 into a goal state
Each state will be associated with utility value
An Optimal policy maximizes the long-term reward: expected sum of rewards. (equiv: min sum of costs)
This selection is done by calculating the value/utility of a state
Notes: Policy generally specifies what the agent should do for any state
If this mapping selects the action that leads to the long-term maximum reward, then the policy is optimal

## Slide 9: Back to CHIMP (Conflict-driven Hierarchical Meta-CSP Planner)
HTN planner with hybrid reasoning
Overcome the large hybrid search by extending it with hierarchical task decomposition strategy
Combine causal knowledge, temporal knowledge and resource
A CSP-style backtracking search is used to find a temporally and symbolically consistent plan
 Note that CHIMP description does not contain the structure of MDP
 Assumed closed world environment (Predictable world)
Notes: initial state is known and fully observable ,
and actions are deterministic or(predictable)
Hybrid planning will be formulated as meta-csp
The hybrid requirement will be represented as Constraint Satisfaction Problem (CSP). A constraint network consists of a finite setof variables, a set of domains of these variables and a set of constraints,
Global consistency means we need to hv consistency in every knowledge aspect ( temporal, spatial ,,,)
We need to combine the structure and probabilistic planningin details we extend the chimp description with mdp structure

## Slide 10: CHALLENGES & LIMITATIONS
Does not model Uncertainty (no probabilities).
Does not consider a more general models.
Solution:
   Combine the existing HTN structure with an MDP solver.
Issues raised:
  How can we represent reward and action behaviors in the hierarchical planning (CHIMP)?
  How to get all the possible states from HTN?
  Why can’t we reject HTN altogether and only use MDPs?
Notes: How can HTNs be modelled as MDPs?

## Slide 11: CHALLENGES & LIMITATIONS
Hierarchical Task Network (CHIMP)
States are not enumerated exhaustively
State consists of properties of the environment
Each action modifies properties of the environment
Set of actions induces a smaller state space
Markov Decision Process
MDP domain explicitly enumerates all relevant states
Implicitly represent the same properties expressed in HTN state
MDP solver must consult the entire state space
Astronomically large: difficult to solve if the problem is very complex (hundreds of state variables)
Notes: The planning is done offline based on the assumption that all the actions are deterministic
Spoon inside a cup

## Slide 12: From HTN to MDP
Expansion
Generate States
Generate transition functions
Generate reward function

## Slide 13: From HTN to MDP (Expansion)
The idea here is to fully expand the HTN domain into graph:
  defined by tasks (vertices) and ordering constraints (edges)
  Each primitive task induces a state

## Slide 14: Expansion Examples: drive_robot() (from Counter)
Decompose task through methods in the domain until primitive tasks are reached

## Slide 15
Notes: All the methods will be decomposed until only primitive éléments are left

## Slide 16
The HTN decompositions depends also on the initial problem description
Expansion Examples: drive_robot() (from northTable)

## Slide 17: States Génération
State-Spaces comes from the reachable primitive tasks in the fully expanded HTN
All expanded HTN states will be used as input for MDP solver
Each primitive task in the fully decomposed HTN is considered to represent the state achieved immediately after executing the action associated with it
Algorithm must detect the overlapping states (for the transition functions) :
  Partition them so that there is no ambiguity over the current state for MDP
Notes: For mdp consists of non-overlapping states ,
in some scenarios we could have states with the same axioms or features , as an abstract example,

## Slide 18: Transition Functions / Reward Génération
The edges in the fully expanded HTN represents that the transitions between the states
The edges also expresses the ordering constraints
If the is a constraints between Task and then there’s non-zero probability transition
Each state will be defined with a reward/cost value
Reward function is used to induce the solver to select actions that lead towards certain desirable states.
Probabilities and reward values are defined in the domain description
Notes: Reward function in an MDP is to induce the solver to select actions that lead an agent towards certain desirable states.

## Slide 19: Operator (CHIMP)
(:operator
(Head !pick_up_object(?obj ?arm))
(Pre p1 On(?obj ?fromArea))
(Pre p2 RobotAt(?mArea))
(Pre p3 Holding(?arm ?nothing))
(Values ?nothing nothing)
(Del p1)
(Del p3)
(Add e1 Holding(?arm ?obj))
(Constraint During(task,p2))
(Constraint Meets(p4,e1))
(Constraint Duration[4000,INF](task))
(ResourceUsage
(Usage armManCapacity 1)))
Primitive task
Resource fluents
Temporal Constraints
Precondition
Effect
Notes: As small demonstration
Robot should be at the table the whole time
In operator , we hv the possiblity to specifiy the duration

## Slide 20: Extended Operator
(:operator
(Head !pick_up_object(?obj ?arm))
(Pre p1 On(?obj ?fromArea))
(Pre p2 RobotAt(?mArea))
(Pre p3 Holding(?arm ?nothing))
. . . .
(Reward -0,04)
(TransitionProb 0,80)
. . . .
(ResourceUsage
(Usage armManCapacity 1)))
Markovian inputs
Notes: This intially how it should look like and later i will explain the conditional probabilistic to allow us to manage the assignment of the markovian inputs

## Slide 21: The necessity of Conditional Probability
Not all states has the same reward and transition probability
Flexibility in assignment markovian parametres for each specific state and task

## Slide 22: The necessity of Conditional Probability
Code of conditional

## Slide 23: Deal with Diverse Knowledge (Hybrid Planning)

## Slide 24: Deal with Diverse Knowledge (Resource Reasoning)

## Slide 25: Deal with Diverse Knowledge (Spatial Reasoning)

## Slide 26: Extended Problem Representation
Is a triple P = ((F, C), T, D) fluents F,
which describe the initial state and the tasks,
and causal, temporal and symbolic constraints C
We added spatial constraints
  Consists of unary and binary constraints
Unary Constraints:
     Size [Lx, Ux], [Ly, Uy]
    At [Lx1, Ux1], [Lx2, Ux2], [Ly1, Uy1], [Ly2, Uy2]
Example
  ( UnarySpatialFluent sp1 Size ( knife1 [4,4] [18,18] ))
  ( UnarySpatialFluent sp2 Size ( fork1 [4,4] [18 ,18] ))
  ( UnarySpatialFluent sp3 At ( knife1 [50,50] [54,54] [50,50] [68,68] ))
  ( UnarySpatialFluent sp4 At ( fork1 [72,72] [76,76] [50,50] [68,68] ))
Notes: consisting of fluents F, which describe the initial state and the tasks, and causal, temporal and symbolic constraints C
We hv two kind of knowledge to represent
Position should be consistent with the size and also the size is static but position could be changed

## Slide 27: Extended Domain Representation
(:operator
(Head !pick_up_two_object(?obj1 ?arm ?obj2 ?otherArm))
(Pre p1 On(?obj2 ?fromArea))
(Pre p2 RobotAt(?mArea)) (Del p4)
(Del p5)
(Add e1 Holding(?arm ?obj1)) //top obj should be held first
(Add e2 Holding(?otherArm ?obj2))
. . .
(Constraint During(task,p3))
(Constraint Duration[5000,INF](task))
(DelSC (?obj1,?obj2))
(DelSC (At) (?obj1))
(DelSC (At) (?obj2))
)
Spatial Constraints
Notes: In Domain, we hv set of methods and operators
rel between the two objects and it's assertion
#delete At: obj not anymore at that position

## Slide 28: Extended Domain Representation
(:operator
(Head !place_object(?obj ?arm ?plArea))
(Pre p1 Holding(?arm ?obj))
(Values ?obj mug mug1)
(Values ?armPosture ArmToSidePosture)
. . . .
(Del p1)
(Add e1 Holding(?arm ?nothing))
(Add e2 On(?obj ?plArea))
(SC (Equals,Equals) (?obj,?mug)) #add Assertion mug1 ->Mug
(Values ?mug mug)
)
Spatial Constraint

## Slide 29: Spatial fluents
As spatial boolean function to check complex conditions as :
            (:method
            (Head put_object(?objDish ?plArea))
            (Pre p1 Holding(?arm ?objDish))
            (Pre p2 RobotAt(?robotArea))
            (Pre p3 Connected(?plArea ?manArea ?preArea))
            (Pre p4 enoughDistance(?objDish ?objKnife ?objFork ?false))
            . . . . . .
            (Sub s1 drive_robot(?preArea))
            (Sub s2 assume_manipulation_pose(?manArea))
            (Sub s3 !shift_object(?objFork ?objDish ?armEmpty))
            (Sub s4 !place_object(?objDish ?arm ?plArea))
            (Constraint Before(s1,s2))
            (Constraint Before(s2,s3))
            (Constraint Starts(s1,task))
            (Constraint Finishes(s4,task))
            )
(Fluent f8 enoughDistance(dish1 knife1 fork1 undef ))
(Fluent f8 isCollision(knife2 mug1 undef ))
Notes: consisting of fluents F, which describe the initial state and the tasks, and causal, temporal and symbolic constraints C

## Slide 30: Evaluation
Task:
  serve an empty dish from counter1 to table1
Resources:
  Cap(LeftArm)=1, Cap(RightArm)=1
4 possible scenarios:
  Collision(Mug Dish) : Boolean
  Enoughdistance(..) : Boolean
Image 4: Layout of the scenario
Notes: Require less operators false false

## Slide 31: Evaluation
Image 5: Performance results
Notes: As larger the plan ist, the longer the exécution time
--C is heavier to execute in computation level and to check the fluent function,,

## Slide 32: Results
Required plan's operators to execute task C
  !pick_up_object(dish1 rightArm1)([...], [...]) [[1, 1], [4001, 471988]]
  !move_base_blind(preManipulationAreaEastCounter1)([...], [...])[[4002, 471989], [8002, 475989]]
  !move_torso(TorsoMiddlePosture)([...], [...]) [[8003, 475990], [12003, 479992]]
  !move_arms_to_carryposture(n)([...], [...]) [[8005, 475992], [12005, 479992]]
  !move_base(preManipulationAreaSouthTable1)([...], [...])[[12006, 479993], [15006, 482993]]
  !move_torso(TorsoUpPosture)([...], [...]) [[15007, 482994], [19007, 490995]]
  !move_arm_to_side(leftArm1)([...], [...]) [[15007, 482994], [19007, 486994]]
  !move_arm_to_side(rightArm1)([...], [...]) [[19008, 486995], [23008, 490995]]
  !move_base_blind(manipulationAreaTable1)([...], [...]) [[23009, 490996], [27009, 494996]]
  !shift_object(fork1 dish1 rightArm1)(0, 0) [[27010, 494999], [32012, 499999]].
  !place_object(dish1 rightArm1 placingAreaTable1)([...], [...]) [[32013, 494997], [32020, 499999]]

## Slide 33: Perspectives
Consider scenarios such populated environment or when the actions are non-deterministic
Deal with uncertainty and ensure collision-free navigation
Extend RA to greater dimensions such 3D
Adapt CHIMP to be integrated into cooperative multi-agent environments
consider a continuous learning environment
Notes: Allow the model to learn and esnure safty through GP for example
Continous using using Reinforcement learning and maybe ensure safness using GP,,
Robot behind the counter,,s

## Slide 34: Conclusion
It has required more human effort to improve its knowledge base to get better performance.
Solving linear programs such as TCSP can be solved in polynomial time
Such calculations are computationally heavy.
There is a large room for improvement
This model provides rich and flexible semantics for encoding the spatial aspect
Notes: To sum up,
using unary and binary constraints combined with spatial uents function
to dene an additional expressive form of knowledge

## Slide 35
Thank You For Your Attention.

## Slide 36: Literature
Meneguzzi, F. e. (2011). An approach to generate MDPs using HTN representations." Decision Making in Partially Observable, Uncertain Worlds: Exploring Insights from Multiple Communities,. Barcelona, Spain.
Stock, S. (2017). Hierarchische hybride Planung für mobile Roboter.